## Slide 1
Isolating valuable compounds from complex mixtures of lignin products
Citation
Objective Use liquid-liquid extraction to isolate individual compounds from the complex product mixtures that result from lignin processing
Approach
Digest poplar lignin in the presence of oxygen to create a mixture of oxygenated aromatic compounds
Apply centrifugal partition chromatography to separate individual monomers based on their solubility in two non-mixing solvents
Result/Impacts
Centrifugal partition chromatography successfully isolated vanillin, syringic acid, syringaldehyde, vanillic acid, and p-hydroxybenzoic acid in two stages of extraction.
The method requires only a few steps, uses no expensive added chemicals, and can be adapted to large-scale use, suggesting that it can provide a scalable way to isolate valuable industrial chemicals from lignin and other biomass-derived feedstocks.
BRC Science Highlight
GLBRC December 2021
Centrifugal partition chromatography provides an effective strategy to separate valuable aromatic products obtained from lignin depolymerization mixtures.
Alherech, M., Omolabake, S., Holland, C.M., Klinger, G.E., Hegg, E.L., Stahl, S.S., “From lignin to valuable aromatic chemicals: lignin depolymerization and monomer separation via centrifugal partition chromatography.” ACS Central Science (2021) [DOI: 10.1021/acscentsci.1c00729]
Notes: Notes:
text
Title again:
Text 1-2 sentence summary?