## Slide 1
Combining Pretreatment with Modified Poplar
Increases Sugar Yields
Bhalla, A. et al. “Engineered lignin in poplar biomass facilitates Cu-catalyzed alkaline-oxidative pretreatment.” ACS Sustainable Chemistry & Engineering. DOI: 10.1021/acssuschemeng.7b02067
Approach
Compare untransformed WT poplar to Line 7 zip-lignin poplar, which produces ester bonds in the lignin backbone, making it amenable to Cu-AHP deconstruction.
Reduce inputs during Cu-AHP (bipyridine and hydrogen peroxide) and enzymes during hydrolysis, then quantify sugar yields.
Result/Impacts
Following Cu-AHP pretreatment and enzymatic hydrolysis, improved glucose yields were observed for zip-lignin Line 7 poplar (85%) compared to untransformed WT poplar (77%).
When zip-lignin Line 7 poplar was used as the feedstock, bipyridine (a) hydrogen peroxide (b), and enzyme loadings (c) could all be substantially reduced while still maintaining high glucose yields.
This validates the potential of zip-lignin poplar as a feedstock for the advanced biofuel and bioproduct industry.
BRC Science Highlight
GLBRC February 2018
Objective
Evaluate the effectiveness of the Cu-AHP pretreatment process on genetically-modified Zip-lignin™ poplar with the goal of developing economically-sustainable deconstruction processes for woody biomass.
Notes: Notes:
text
Title again:
Text 1-2 sentence summary?