## Slide 1
Different biomass pretreatment strategies give different hydrolysis, lignin yields from woody biomass
A. Bhalla, et al. “Performance of three delignifying pretreatments on hardwoods: hydrolysis yields, comprehensive mass balances, and lignin properties.” Biotechnol Biofuels (2019) 12, 213 [DOI: 10.1186/s13068-019-1546-0]
Objective
Assess three pretreatments under investigation at the DOE Bioenergy Research Centers in a side-by-side comparison of performance on model bioenergy hardwoods.
Results/Impacts
Overall, the three pretreatments highlighted in this study showed different capabilities to reduce biomass recalcitrance to achieve high enzymatic hydrolysis yields, and to produce lignin fractions suitable for valorization.
Different pretreatment strategies may give preferred outcomes depending on specific project goals and anticipated further use of the material (specifically the chemical uses of the produced lignin fractions).
BRC Science Highlight
GLBRC September 2019
Approach
Employed three pretreatments: co-solvent- enhanced lignocellulosic fractionation (CELF), ionic liquid using potentially biomass-derived components (cholinium lysinate or [Ch][Lys]), and two-stage copper-catalyzed alkaline hydrogen peroxide (Cu-AHP).
Evaluated susceptibility of pretreated biomass to further breakdown by cellulolytic enzymes.
Performed detailed mass balances on material passing through each of the three processes.
Characterized the yields, structural properties, and susceptibility of the pretreatment-soluble lignin fractions for depolymerization to aromatic monomers.
Performance of Cu-AHP, CELF, and [Ch][Lys] pretreatments. A) Enzymatic hydrolysis yields from glucose from pretreated hybrid poplar as a function of enzyme loading. B) Correlation between aromatic monomer yields from poplar or eucalyptus lignin by quantitative thioacidolysis and the β-O-4 content of pretreatment-solubilized and recovered lignin as determined by 13C NMR.