## Slide 1
Using coproducts from lignin to increase value from biorefineries
S. D. Karlen et al. “Assessing the viability of recovery hydroxycinnamic acids from lignocellulosic biorefinery alkaline pretreatment waste streams.” ChemSusChem (2020) [DOI: 10.1002/cssc.201903345]
Objective
Combine laboratory research and modeling simulations to determine the viability of producing coproducts from lignin to improve the economics of lignocellulosic biorefineries.
Results/Impacts
Assessment of the full biorefinery system, from field to the liquid fuels and coproducts, identified key parameters needed to design an economically viable biorefinery-based model.
  Technoeconomic analysis indicates that cost effective coproduct recovery will require channeling coproducts to a single useful product at high titers — at least five times higher than observed for the hydroxycinnamic acids studied in this work.
  Process engineers should develop a viable coproduct isolation process that reduces costs by more than 80%.
BRC Science Highlight
GLBRC April 2020
Approach
Integrate field-to-refinery research: crop engineering to enhance production of lignin-bound, high-value chemicals; field trials to assess plant viability; lab-scale biomass pretreatment to release the high-value chemicals; yield quantification.
Establish a baseline technoeconomic analysis of this ‘lignin-first’ strategy to determine where to focus future research efforts.