## Slide 1
Formaldehyde stabilization facilitates lignin monomer production during biomass depolymerization
Shuai, L. et al. “Formaldehyde stabilization facilitates lignin monomer production during biomass depolymerization.” Science 354, 329-333 (2016) [DOI: 10.1126/science.aaf7810].
Objective Extracting a soluble and uncondensed lignin substrate during biomass pretreatment could facilitate the production of lignin monomers and be compatible with current biorefining strategies
Approach
To prevent inter-unit carbon-carbon coupling during extraction (the major challenge in developing such a process), our strategy was to attempt to block the reactive benzylic positions with a protecting agent during pretreatment
Initial tests of formaldehyde protection on a model lignin dimer were followed by testing the effect of formaldehyde stabilization during the extraction of real lignin from wood samples (beech, spruce, and transgenic poplar)
Result/Impacts
Using formaldehyde to stabilize lignin during extraction leads to near theoretical yields of lignin monomers after hydrogenolysis of the extracted product; yields were three to seven times higher than those obtained when using the analogous method without formaldehyde.
The longstanding interest in lignin valorization has translated into few commercial processes because of the lack of practical high-yield lignin depolymerization methods that can be used while upgrading biomass polysaccharides; our formaldehyde stabilization results suggest that lignin upgrading could be easily integrated into current biorefinery schemes, especially considering that formaldehye is a relatively inexpensive bulk chemical that can be produced from biomass-derived syngas or methanol, either sourced biologically or from lignin methoxyl groups.
BRC Science Highlight
GLBRC October 2016
Notes: Notes:
text
Title again:
Text 1-2 sentence summary?